## Slide 1: CS 3700 Networks and Distributed Systems
Bridging
(From Hub to Switch by Way of Tree)
Revised 8/19/15

## Slide 2: Just Above the Data Link Layer
Bridging
  How do we connect LANs?
Function:
  Route packets between LANs
Key challenges:
  Plug-and-play, self configuration
  How to resolve loops
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Recap
Pros: Simplicity
  Hardware is stupid and cheap
Cons: No scalability
  More hosts = more collisions = pandemonium
Originally, Ethernet was a broadcast technology
Tee Connector
Terminator
Hub
Repeater

## Slide 4: The Case for Bridging
Need a device that can bridge different LANs
  Only forward packets to intended recipients
  Much less broadcasting!
Hub
A
C
B
A
C
B
Send Packet
B  C
Send Packet
B  C
Bridge

## Slide 5: Bridging the LANs
Bridging limits the size of collision domains
  Vastly improves scalability
  Question: could the whole Internet be one bridging domain?
Tradeoff: bridges are more complex than hubs
  Physical layer device vs. data link layer device
  Need memory buffers, packet processing hardware, routing tables
Hub
Hub

## Slide 6: Bridge Internals
Bridges have memory buffers to queue packets
Bridge is intelligent, only forwards packets to the correct output
Bridges are high performance, full N * line rate is possible
Switch Fabric
Inputs
Outputs
Bridge
Makes routing decisions
Hub
Memory buffer

## Slide 7: Bridges
Original form of Ethernet switch
Connect multiple IEEE 802 LANs at layer 2
Goals
  Reduce the collision domain
  Complete transparency
    “Plug-and-play,” self-configuring
    No hardware of software changes on hosts/hubs
    Should not impact existing LAN operations
Hub
Forwarding of frames
Learning of (MAC) Addresses
Spanning Tree Algorithm (to handle loops)

## Slide 8: Frame Forwarding Tables
00:00:00:00:00:DD | 1 | 3 minutes
Each bridge maintains a forwarding table
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 1 minute
00:00:00:00:00:BB | 2 | 7 minutes
00:00:00:00:00:CC | 3 | 2 seconds

## Slide 9: Frame Forwarding in Action
Assume a frame arrives on port 1
If the destination MAC address is in the forwarding table, send the frame on the correct output port
If the destination MAC isn’t in the forwarding table, broadcast the frame on all ports except 1
Port 1
Port 3
Port 2
Port 4

## Slide 10: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error Prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port
Hub
00:00:00:00:00:AA
00:00:00:00:00:BB
Port 1
Port 2
00:00:00:00:00:BB | 2 | 0 minutes
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 0 minutes
Delete old entries after a timeout

## Slide 11: Complicated Learning Example
<Src=AA, Dest=FF>
<Src=CC, Dest=AA>
<Src=EE, Dest=CC>
FF
EE
DD
CC
BB
AA
Port 1
Port 2
Port 1
Port 2
Hub
Hub
Hub
AA | 1
AA | 1
CC | 2
CC | 1
EE | 2
EE | 2
Bridge 1
Bridge 2

## Slide 12: The Danger of Loops
<Src=AA, Dest=DD>
This continues to infinity
  How do we stop this?
Remove loops from the topology
  Without physically unplugging cables
802.1 uses an algorithm to build and maintain a spanning tree for routing
AA
Port 1
Hub
Port 1
Hub
Port 2
Port 2
AA | 1
AA | 1
BB
CC
DD
AA | 2
AA | 2
AA | 1
AA | 1

## Slide 13: Spanning Tree Definition
A subset of edges in a graph that:
  Span all nodes
  Do not create any cycles
This structure is a tree
1
4
2
5
6
3
7
1
4
2
5
6
3
7
5
1
4
2
6
3
7

## Slide 14: Spanning Tree Poem
Algorhyme
  I think that I shall never see
  a graph more lovely than a tree.
  A tree whose crucial property
  is loop-free connectivity.
  A tree that must be sure to span
  so packet can reach every LAN.
  First, the root must be selected.
  By ID, it is elected.
  Least-cost paths from root are traced.
  In the tree, these paths are placed.
  A mesh is made by folks like me,
  then bridges find a spanning tree.
- Radia Perlman

## Slide 15: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 16: Definitions
Bridge ID (BID) = <Random Number>
Root Bridge: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridge: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 17: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BPDUs:
Based on received BPDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to root)
Root ID
Path Cost to Root
Bridge ID

## Slide 18: Comparing BPDUs
if R1 < R2: use BPDU1
else if R1 == R2 and Cost1 < Cost2: use BPDU1
else if R1 == R2 and Cost1 == Cost 2 and B1 < B2: use BPDU1
else: use BPDU2
R1
Cost1
B1
R2
Cost2
B2
BPDU1
BPDU2

## Slide 19: Spanning Tree Construction
0: 0/0
12: 12/0
3: 3/0
27: 27/0
41: 41/0
9: 9/0
68: 68/0
27: 0/1
12: 0/1
41: 3/1
68: 9/1
41: 0/2
3: 0/2
68: 3/2
9: 3/2
68: 0/3
9: 0/3

## Slide 20: Designated Bridges
Ultimately, each bridge must decide to enable or disable each port
Reasons to keep a port enabled:
  You receive no BPDUs on that port
    Indicates there are no other bridges
  The port is a root port
    You need to be able to forward packets to the root of the spanning tree
  You are the designated bridge for that LAN
    All other bridges on that LAN have a longer path to the root, or their bridge ID is higher than yours
?
?
?
?
?
?
?
0
9
27
On, 1
On, 2
On, 2
On, 3
On, 3
Off
On, 3

## Slide 21: More Designated Bridges
?
?
Ultimately, each bridge must decide to enable or disable each port
Reasons to keep a port enabled:
  You receive no BPDUs on that port
    Indicates there are no other bridges
  It is the root port
    You need to be able to forward packets to the root of the spanning tree
  You are the designated bridge for that LAN
    All other bridges on that LAN have a longer path to the root, or their bridge ID is higher than yours
?
?
?
?
?
?
0
9
27
On, 2
On, 2
On, 3
On, 3
On, 3
On, 3
On, 2
Off
3

## Slide 22: Bridges vs. Switches
Bridges make it possible to increase LAN capacity
  Reduces the amount of broadcast packets
  No loops
Switch is a special case of a bridge
  Each port is connected to a single host
    Either a client machine
    Or another switch
  Thus, there are no collision domains
  No need for CSMA/CD! Simplifies hardware.
  Can have different speeds on each port
2 hosts on 1 port
Not a legal network with switches

## Slide 23: Switching the Internet
Capabilities of switches:
  Network-wide routing based on MAC addresses
  Learn routes to new hosts automatically
  Resolve loops
Could the whole Internet be one switching domain?
NO

## Slide 24: Limitations of MAC Routing
Inefficient
  Flooding packets to locate unknown hosts
Poor Performance
  Spanning tree does not balance load
  Hot spots
Extremely Poor Scalability
  Every switch needs every MAC address on the Internet in its routing table!
  IP addresses these problems (next lecture…)