## Slide 1: CS 3700 Networks and Distributed Systems
Transport Layer
(UDP, but mostly TCP)
Revised 10/06/19

## Slide 2: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions:
  Creating long lived connections
  Reliable, in-order packet delivery
  Error detection
  Flow and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 4: The Case for Multiplexing
Datagram network
  No circuits
  No connections
Clients run many applications at the same time
  Who to deliver packets to?
IP header “protocol” field
  8 bits = 256 concurrent streams
Insert Transport Layer to handle demultiplexing
Packet
Network
Data Link
Physical
Transport

## Slide 5: Demultiplexing Traffic
Endpoints identified by <src_ip, src_port, dest_ip, dest_port>
Network
Transport
Application
P1
P2
P3
P4
P6
P7
P5
Host 1
Host 2
Host 3
Unique port for each application
Applications share the same network
Server applications communicate with multiple clients

## Slide 6: Layering, Revisited
Application
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Lowest level end-to-end protocol (in theory)
  Transport header only read by source and destination
  Routers view transport header as payload
Application
Transport
Network
Data Link
Physical
Network
Data Link
Layers communicate peer-to-peer

## Slide 7: User Datagram Protocol (UDP)
Simple, connectionless datagram
  C sockets: SOCK_DGRAM
Port numbers enable demultiplexing
  16 bits = 65535 possible ports
  Port 0 is invalid
Checksum for error detection
  Detects (some) corrupt packets
  Does not detect dropped, duplicated, or reordered packets
Destination Port
0
16
31
Payload Length
Source Port
Checksum

## Slide 8: Uses for UDP
Invented after TCP
  Why?
Not all applications can tolerate TCP
Custom protocols can be built on top of UDP
  Reliability? Strict ordering?
  Flow control? Congestion control?
Examples
  RTMP – real-time media streaming (e.g. voice, video)
  uTP – “microtransport” protocol used by BitTorrent
  QUIC – app-level transport protocol developed by Google to speed up HTTP

## Slide 9: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 10: Transmission Control Protocol
Options
Reliable, in-order, bi-directional byte streams
  Port numbers for demultiplexing
  Virtual circuits (connections)
  Flow control
  Congestion control, approximate fairness
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 11: Connection Setup
Why do we need connection setup?
  To establish state on both hosts
  Most important state: sequence numbers
    Count the number of bytes that have been sent
    Initial value chosen at random
    Why?
Important TCP flags (1 bit each)
  SYN – synchronization, used for connection setup
  ACK – acknowledge received data
  FIN – finish, used to tear down connection

## Slide 12: Three Way Handshake
Each side:
  Notifies the other of starting sequence number
  ACKs the other side’s starting sequence number (+1)
  Sequence # must increment on receiving a SYN
Client
Server
SYN <SeqC, 0>
SYN/ACK <SeqS, SeqC+1>
ACK <SeqC+1, SeqS+1>
Why
Sequence # +1?
Notes: 211

## Slide 13: Connection Setup Issues
Connection confusion
  How to disambiguate connections from the same host?
  Random sequence numbers
Packet injection
  How Kevin Mitnick hacked into the SDSC
  Need good random number generators!
Connection state management
  Each SYN allocates state on the server
  SYN flood is a common denial of service attack
  Solution: SYN cookies

## Slide 14: Connection Tear Down
Either side can initiate tear down
Other side may continue sending data
  Half open connection
  shutdown()
Acknowledge the last FIN
  Sequence number + 1
Client
Server
FIN <SeqA, *>
ACK <*, SeqA+1>
ACK
Data
FIN <SeqB, *>
ACK <*, SeqB+1>

## Slide 15: Sequence Number Space
TCP uses a byte stream abstraction
  Initial, random values selected during setup
  Each byte in each stream is numbered
  32-bit value, wraps around
Byte stream broken down into segments (packets)
  Size limited by the Maximum Segment Size (MSS, typically 1460 bytes)
  Set to limit fragmentation
Each segment has a sequence number
Segment 8
Segment 9
Segment 10
13450
14950
16050
17550

## Slide 16: Bidirectional Communication
Each side of the connection can send and receive
  Different sequence numbers for each direction
Client
Server
Data (1460 bytes)
Data/ACK (730 bytes)
Data/ACK (1460 bytes)
Seq.
Ack.
Seq.
Ack.
1
23
23
1461
1461
753
753
2921
Data and ACK in the same packet
23
1

## Slide 17: Flow Control
Problem: how many packets should a sender transmit?
  Too many packets may overwhelm the receiver
  Size of the receiver's buffers may change over time
Solution: sliding window
  Receiver tells the sender how big their buffer is
  Called the advertised window
  For window size n, sender may transmit n bytes without receiving an ACK
  After each ACK, the window slides forward
Advertised window may go to zero!

## Slide 18: Flow Control: Sender Side
Sequence Number
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Sent
Dest. Port
Src. Port
Acknowledgement Number
Adv. Window
Urgent Pointer
Flags
Checksum
HL
Packet Received
Dest. Port
Sequence Number
ACKed
Sent
To Be Sent
Outside Window
Window
App Write
Must be buffered until ACKed
Notes: Each side acts and sender and receiver
Every message contains sequence number, even if payload length is zero
Every message contains acknowledgements, even if no data was received
Every message advertises the window size

## Slide 19: Sliding Window Example
1
2
3
4
5
6
7
5
6
7
Time
Time
TCP is ACK Clocked
Short RTT  quick ACK  window slides quickly
Long RTT  slow ACK  window slides slowly

## Slide 20: What Should the Receiver ACK?
ACK every packet
Use cumulative ACK, where an ACK for sequence n implies ACKS for all k < n
Use negative ACKs (NACKs), indicating which packet did not arrive
Use selective ACKs (SACKs), indicating those that did arrive, even if not in order
  SACK is an actual TCP extension

## Slide 21: Sequence Numbers, Revisited
32 bits, unsigned
  Why so big?
For the sliding window you need…
  |Sequence # Space| > 2 * |Sending Window Size|
  232 > 2 * 216
Sequence number would wrap around at 286Mbps
  What about GigE? PAWS algorithm + TCP options

## Slide 22: Silly Window Syndrome
Problem: what if the window size is very small?
  Multiple, small packets, headers dominate data
Equivalent problem: sender transmits packets one byte at a time
for (int x = 0; x < strlen(data); ++x)
write(socket, data + x, 1);
Header
Data
Header
Data
Header
Data
Header
Data

## Slide 23: Nagle’s Algorithm
If the window >= MSS and available data >= MSS:
  Send the data
Elif there is unACKed data:
  Enqueue data in a buffer (send after a timeout)
Else: send the data
Problem: Nagle’s Algorithm delays transmissions
  What if you need to send a packet immediately?
  int flag = 1;
  setsockopt(sock, IPPROTO_TCP, TCP_NODELAY, (char *) &flag, sizeof(int));
Send a full packet
Send a non-full packet if nothing else is happening

## Slide 24: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
  Missing sequence numbers indicate lost packets
Lost segments detected by sender
  Use timeout to detect missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 25: Retransmission Time Outs (RTO)
Problem: time-out is linked to round trip time
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Timeout is too short
What about if timeout is too long?

## Slide 26: Round Trip Time Estimation
Original TCP round-trip estimator
  RTT estimated as a moving average
  new_rtt = α (old_rtt) + (1 – α)(new_sample)
  Recommended α: 0.8-0.9 (0.875 for most TCPs)
RTO = 2 * new_rtt (i.e. TCP is conservative)
Data
ACK
RTT Sample

## Slide 27: RTT Sample Ambiguity
Karn’s algorithm: ignore samples for retransmitted segments
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Sample
Sample?

## Slide 28: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 29: What is Congestion?
Load on the network is higher than capacity
  Capacity is not uniform across networks
    Modem vs. Cellular vs. Cable vs. Fiber Optics
  There are multiple flows competing for bandwidth
    Residential cable modem vs. corporate datacenter
  Load is not uniform over time
    10pm, Sunday night = BitTorrent Game of Thrones

## Slide 30: Why is Congestion Bad?
Results in packet loss
  Routers have finite buffers, packets must be dropped
Practical consequences
  Router queues build up, delay increases
  Wasted bandwidth from retransmissions
  Low network goodput

## Slide 31: The Danger of Increasing Load
Knee – point after which
  Throughput increases very slowly
  Delay increases quickly
In an M/M/1 queue
  Delay = 1/(1 – utilization)
Cliff – point after which
  Throughput  0
  Delay  ∞
Congestion Collapse
Load
Load
Goodput
Delay
Knee
Cliff
Ideal point

## Slide 32: Cong. Control vs. Cong. Avoidance
Congestion Collapse
Goodput
Knee
Cliff
Load
Congestion Avoidance:
Stay left of the knee
Congestion Control:
Stay left of the cliff

## Slide 33: Advertised Window, Revisited
Does TCP’s advertised window solve congestion?
NO
The advertised window only protects the receiver
A sufficiently fast receiver can max the advertised window (i.e. 216 bytes)
  What if the network is slower than the receiver?
  What if there are other concurrent flows?
Key points
  Window size determines send rate
  Window must be adjusted to prevent congestion collapse

## Slide 34: Goals of Congestion Control
Adjusting to the bottleneck bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows
Maximizing throughput

## Slide 35: General Approaches
Do nothing, send packets indiscriminately
  Many packets will drop, totally unpredictable performance
  May lead to congestion collapse
Reservations
  Pre-arrange bandwidth allocations for flows
  Requires negotiation before sending packets
  Must be supported by the network
Dynamic adjustment
  Use probes to estimate level of congestion
  Speed up when congestion is low
  Slow down when congestion increases
  Messy dynamics, requires distributed coordination

## Slide 36: TCP Congestion Control
Introduce a congestion window at the sender
  Congestion control is sender-side problem
  Controls the number of unACKed packets
  Separate variable, but bounded by the receiver’s advertised window
Sending rate is ~ congestion window/RTT
  Why is the send rate proportional to RTT?
  Recall that TCP is ACK-clocked
Idea: vary the window size to control the send rate

## Slide 37: Congestion Window (cwnd)
Limits how much data is in transit, denominated in bytes
wnd = min(cwnd, adv_wnd);
effective_wnd = wnd – (last_byte_sent – last_byte_acked);
last_byte_acked
last_byte_sent
cwnd
effective_wnd
adv_wnd
Bytes
To Send

## Slide 38: Two Basic Components
Detect congestion
  Packet dropping is most reliably signal
    Delay-based methods are hard and risky
  How do you detect packet drops? ACKs
    Timeout after not receiving an ACK
    Several duplicate ACKs in a row (ignore for now)
Rate adjustment algorithm
  Modify cwnd
  Probe for bandwidth
  Respond to congestion
Except on wireless networks

## Slide 39: Rate Adjustment
Recall: TCP is ACK clocked
  Congestion = delay = long wait between ACKs
  No congestion = low delay = ACKs arrive quickly
Basic algorithm
  Upon receipt of ACK: increase cwnd
    Data was delivered, perhaps we can send faster
    cwnd growth is proportional to RTT
  On loss: decrease cwnd
    Data is being lost, there must be congestion
Question: what increase/decrease functions to use?

## Slide 40: Utilization and Fairness
Flow 1 Throughput
Flow 2 Throughput
Max throughput for flow 2
Zero throughput for flow 1
Max throughput for flow 1
Zero throughput for flow 2
Less than full utilization
More than full utilization (congestion)
Ideal point
Max efficiency
Perfect fairness
Equal throughput
(fairness)

## Slide 41: Multiplicative Increase, Additive Decrease
Not stable!
Veers away from fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 42: Additive Increase, Additive Decrease
Stable
But does not converge to fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 43: Multiplicative Increase, Multiplicative Decrease
Stable
But does not converge to fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 44: Additive Increase, Multiplicative Decrease
Converges to stable and fair cycle
Symmetric around y=x
Flow 1 Throughput
Flow 2 Throughput

## Slide 45: Implementing Congestion Control
Maintains three variables:
  cwnd: congestion window
  adv_wnd: receiver advertised window
  ssthresh: slow start threshold (used to update cwnd)
For sending, use: effective_wnd = min(cwnd, adv_wnd)
Two phases of congestion control
  Slow start (cwnd < ssthresh)
    Probe for bottleneck bandwidth
  Congestion avoidance (cwnd >= ssthresh)
    AIMD

## Slide 46: Slow Start
Goal: reach knee quickly
Upon starting (or restarting) a connection
  cwnd =1
  ssthresh = adv_wnd
  Each time a segment is ACKed, cwnd++
Continues until…
  ssthresh is reached
  Or a packet is lost
Slow Start is not actually slow
  cwnd increases exponentially
Load
Goodput
Knee
Cliff

## Slide 47: Slow Start Example
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd grows rapidly
Slows down when…
  cwnd >= ssthresh
  Or a packet drops

## Slide 48: Congestion Avoidance
AIMD mode
ssthresh is lower-bound guess about location of the knee
If cwnd >= ssthresh then each time a segment is ACKed cwnd += 1/cwnd
So cwnd is increased by one only if all segments have been acknowledged

## Slide 49: Congestion Avoidance Example
Round Trip Times
cwnd (in segments)
Slow Start
cwnd >= ssthresh
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd = 9
ssthresh = 8

## Slide 50: TCP Pseudocode
Initially: cwnd = 1; ssthresh = adv_wnd;
New ack received: if (cwnd < ssthresh) /* Slow Start*/ cwnd = cwnd + 1; else /* Congestion Avoidance */ cwnd = cwnd + 1/cwnd;
Timeout: /* Multiplicative decrease */ ssthresh = cwnd/2; cwnd = 1;

## Slide 51: The Big Picture
Time
cwnd
Timeout
Slow Start
Congestion
Avoidance
ssthresh

## Slide 52: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 53: Congestion Control Goals, revisited
Adjusting to the bottleneck bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows
Maximizing throughput
Dynamic adjustment
  Use probes (packet drops) to estimate level of congestion
  Speed up (increase cwnd) when congestion is low
  Slow down (decrease cwnd) when congestion increases
  Requires distributed coordination (every TCP client)

## Slide 54: The Evolution of TCP
Thus far, we have discussed TCP Tahoe
  Original version of TCP
However, TCP was invented in 1974!
  Today, there are many variants of TCP
Early, popular variant: TCP Reno
  Tahoe features, plus…
  Fast retransmit
  Fast recovery

## Slide 55: TCP Reno: Fast Retransmit
Problem: in Tahoe, if segment is lost, there is a long wait until the RTO
Reno: retransmit after 3 duplicate ACKs
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
1
2
3
3
3
3
3 Duplicate ACKs

## Slide 56: TCP Reno: Fast Recovery
Initially: cwnd = 1; ssthresh = adv_wnd;
New ack received: if (cwnd < ssthresh) /* Slow Start*/ cwnd = cwnd + 1; else /* Congestion Avoidance */ cwnd = cwnd + 1/cwnd;
3 duplicate acks: cwnd = cwnd/2; goto Cong Avoid
Timeout:
/* Multiplicative decrease */ ssthresh = cwnd/2;
cwnd = 1;
After a fast-retransmit set cwnd to cwnd/2 then, enter Congestion Avoidance
  i.e. don’t reset cwnd to 1
  Avoid unnecessary return to slow start
  Prevents expensive timeouts
But when RTO expires still do cwnd = 1
  Return to slow start, same as Tahoe
  Indicates packets aren’t being delivered at all
  i.e. congestion must be really bad

## Slide 57: Fast Retransmit and Fast Recovery (S2 End here)
At steady state, cwnd oscillates around the optimal window size
TCP always forces packet drops
Time
cwnd
Timeout
Slow Start
Congestion Avoidance
Fast Retransmit/Recovery
ssthresh
Timeout

## Slide 58: Many TCP Variants…
Tahoe: the original
  Slow start with AIMD
  Dynamic RTO based on RTT estimate
Reno: fast retransmit and fast recovery
NewReno: improved fast retransmit
  Each duplicate ACK triggers a retransmission
  Problem: >3 out-of-order packets causes pathological retransmissions
Vegas: delay-based congestion avoidance
And many, many, many more…

## Slide 59: TCP in the Real World
What are the most popular variants today?
  Compound TCP (Windows)
    Based on Reno
    Uses two congestion windows: delay based and loss based
    Thus, it uses a compound congestion controller
  TCP CUBIC (Linux)
    Enhancement of BIC (Binary Increase Congestion Control)
    Window size controlled by cubic function
    Parameterized by the time T since the last dropped packet

## Slide 60: High Bandwidth-Delay Product
Key Problem: TCP performs poorly when
  The capacity of the network (bandwidth) is large
  The delay (RTT) of the network is large
  bandwidth * delay is large
    b * d = maximum amount of in-flight data in the network
    a.k.a. the bandwidth-delay product
Why does TCP perform poorly?
  Slow start and additive increase are slow to converge when bandwidth is large
  TCP is ACK clocked
    i.e. TCP can only react as quickly as ACKs are received
    Large RTT  ACKs are delayed  TCP is slow to react

## Slide 61: Poor Performance of TCP Reno CC
Bottleneck Bandwidth (Mb/s)
Avg. TCP Utilization
50 flows in both directions
Buffer = BW x Delay
RTT = 80 ms
Round Trip Delay (sec)
Avg. TCP Utilization
50 flows in both directions
Buffer = BW x Delay
BW = 155 Mb/s

## Slide 62: Fairness
Key problem: TCP throughput depends on RTT
1 Mbps
1 Mbps
1 Mbps
1 Mbps
1 Mbps
100 ms
1000 ms
ACK clocking makes TCP inherently unfair
Possible solution: maintain a separate delay window
  Implemented by Microsoft’s Compound TCP

## Slide 63: Goals
Fast window growth
  Slow start and additive increase are too slow when bandwidth is large
  Want to converge more quickly
Maintain fairness with other TCP variants
  Window growth cannot be too aggressive
Improve RTT fairness
  TCP Tahoe/Reno flows are not fair when RTTs vary widely
Simple implementation

## Slide 64: Compound TCP Implementation
Default TCP implementation in Windows
Key idea: split cwnd into two separate windows
  Traditional, loss-based window
  New, delay-based window
wnd = min(cwnd + dwnd, adv_wnd)
  cwnd is controlled by AIMD
  dwnd is the delay window
Rules for adjusting dwnd:
  If RTT is increasing, decrease dwnd (dwnd >= 0)
  If RTT is decreasing, increase dwnd
  Increase/decrease are proportional to the rate of change

## Slide 65: Compound TCP Example
Low
RTT
High
RTT
Aggressiveness corresponds to changes in RTT
Advantages: fast ramp up, more fair to flows with different RTTs
Disadvantage: must estimate RTT, which is very challenging
Time
cwnd
Timeout
Slow Start
Timeout
Slower cwnd growth
Faster cwnd growth

## Slide 66: TCP CUBIC Implementation
Default TCP implementation in Linux
Replace AIMD with cubic function
  C  a constant scaling factor
  β  a constant fraction for multiplicative decrease
  T  time since last packet drop
  cwndmax  cwnd when last packet dropped

## Slide 67: TCP CUBIC Example
Less wasted bandwidth due to fast ramp up
Stable region and slow acceleration help maintain fairness
  Fast ramp up is more aggressive than additive increase
  To be fair to Tahoe/Reno, CUBIC needs to be less aggressive
Time
cwnd
Timeout
Slow Start
CUBIC Function
cwndmax
Fast ramp up
Stable
Region
Slowly accelerate to probe for bandwidth

## Slide 68: Simulations of CUBIC Flows
CUBIC
CUBIC
Reno
Reno

## Slide 69: Deploying TCP Variants
TCP assumes all flows employ TCP-like congestion control
  TCP-friendly or TCP-compatible
  Violated by UDP :(
If new congestion control algorithms are developed, they must be TCP-friendly
Be wary of unforeseen interactions
  Variants work well with others like themselves
  Different variants competing for resources may trigger unfair, pathological behavior

## Slide 70: Initial Window Size
What should be the initial value of cwnd?
  Too small – flows take longer to leave slow start
  Too big – new flows create burst of traffic that may congest networks
Subject of ongoing debate
  E.g. Linux kernel officially adopted cwnd = 10 in 2011
What sizes are in use today?
Jan Rüth, Christian Bormann, Oliver Hohlfeld. Large-scale Scanning of TCP’s Initial Window. IMC 2017.

## Slide 71: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 72: Common TCP Options
Window scaling
SACK: selective acknowledgement
Maximum segment size (MSS)
Timestamp
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 73: Window Scaling
Problem: the advertised window is only 16-bits
  Effectively caps the window at 65536B, 64KB
  Example: 1.5Mbps link, 513ms RTT
(1.5Mbps * 0.513s) = 94KB
64KB / 94KB = 68% of maximum possible speed
Solution: introduce a window scaling value
  scaled_adv_wnd = adv_wnd << wnd_scale;
  Maximum shift is 14 bits, 1GB maximum window

## Slide 74: SACK: Selective Acknowledgment
Problem: duplicate ACKs only tell us about 1 missing packet
  Multiple rounds of dup ACKs needed to fill all holes
Solution: selective ACK
  Include received, out-of-order sequence numbers in TCP header
  Explicitly tells the sender about holes in the sequence
8
9
10
11
4
4
5
6
7
4
4
4
4

## Slide 75: Other Common Options
Maximum segment size (MSS)
  Essentially, what is the hosts MTU
  Saves on path discovery overhead
Timestamp
  When was the packet sent (approximately)?
  Used to prevent sequence number wraparound
  PAWS algorithm

## Slide 76: Issues with TCP
The vast majority of Internet traffic is TCP
However, many issues with the protocol
  Lack of fairness
  Synchronization of flows
  Poor performance with small flows
  Really poor performance on wireless networks
  Susceptibility to denial of service

## Slide 77: Synchronization of Flows
Ideal bandwidth sharing
cwnd
cwnd
cwnd
Oscillating, but high overall utilization
In reality, flows synchronize
One flow causes all flows to drop packets
Periodic lulls of low utilization

## Slide 78: Small Flows
Problem: TCP is biased against short flows
  1 RTT wasted for connection setup (SYN, SYN/ACK)
  cwnd always starts at 1
Vast majority of Internet traffic is short flows
  Mostly HTTP transfers, <100KB
  Most TCP flows never leave slow start!
Proposed solutions (driven by Google):
  Increase initial cwnd to 10
  TCP Fast Open: use cryptographic hashes to identify receivers, eliminate the need for three-way handshake

## Slide 79: Wireless Networks
Problem: Tahoe and Reno assume loss = congestion
  True on the WAN, bit errors are very rare
  False on wireless, interference is very common
TCP throughput ~ 1/sqrt(drop rate)
  Even a few interference drops can kill performance
Possible solutions:
  Break layering, push data link info up to TCP
  Use delay-based congestion detection (TCP Vegas)
  Explicit congestion notification (ECN)
    Routers mark the 1-bit ECN field in the TCP header to indicate congestion

## Slide 80: Denial of Service (S2 Start Here)
Problem: TCP connections require state
  Initial SYN allocates resources on the server
  State must persist for several minutes (RTO)
SYN flood: send enough SYNs to a server to allocate all memory/meltdown the kernel
Solution: SYN cookies
  Idea: don’t store initial state on the server
  Securely insert state into the SYN/ACK packet
  Client will reflect the state back to the server

## Slide 81: SYN Cookies
Did the client really send me a SYN recently?
  Timestamp: freshness check
  Cryptographic hash: prevents spoofed packets
Maximum segment size (MSS)
  Usually stated by the client during initial SYN
  Server should store this value…
  Reflect the clients value back through them
Sequence Number
Timestamp
31
0
5
MSS
8
Crypto Hash of Client IP & Port

## Slide 82: SYN Cookies in Practice
Advantages
  Effective at mitigating SYN floods
  Compatible with all TCP versions
  Only need to modify the server
  No need for client support
Disadvantages
  MSS limited to 3 bits, may be smaller than clients actual MSS
  Server forgets all other TCP options included with the client’s SYN
    SACK support, window scaling, etc.